Sensor Interfacing
Dr. Ashish V. Joglekar
Member of Technical Staff,
Robert Bosch Center for Cyber Physical Systems,
IISc

---
Agenda
- Sensor Classification
- Sensor Properties
- Case Studies:
  - Temperature
  - 3 axis Accelerometer
  - Soil Moisture
  - Heart Beat
  - Humidity
  - Gas sensor
- Data Output Formats
- ADCs
- Sensor Installation
- Demos

---
Sensor Classification
- Primary Input quantity (Measurand)
- Transduction Principle
- Material type
- Electrical property
- Application
- Output format / Protocol

---
How to select a specific sensor?
- Sensor Datasheet
- Sensor Properties

---
Sensor Properties
- Dynamic Range : Max and Min values that can be measured
- Transfer function : Functional relationship between input and output
- Sensitivity : Slope of output characteristic curve
- Linearity : Difference between actual transfer function and best straight line
- Resolution : Smallest detectable incremental change
- Accuracy : Max difference between actual and measured value
- Precision: Degree of reproducibility of a measurement
- Bandwidth : Finite Response time to an instantaneous change
- Noise : All sensors produce some output noise in addition to the output signal
- Drift : e.g. Temperature coefficient of a sensor
- Cost

---
Sensor Analog Front-end
- Sensor Biasing
- Signal conditioning
  - Filters
  - Amplifiers
  - Comparators
  - Linearization circuit
  - Compensation for drift
  - Calibration

---
Example: Temperature sensors
Ref: National Instruments

---
LM35 Temperature Sensor
Ref: LM35 Datasheet

---
ADXL335 3 Axis Accelerometer
        Ref: ADXL335 Datasheet

---
Soil Moisture Sensor

---
Pulse Sensor
Ref: http://pulsesensor.com/pages/open-hardware

---
DHT11
Ref: DHT11 Datasheet

---
MQ2 Gas Sensor
Ref: MQ2 Datasheet

---
Typical sensors
Ref: Sensor Technology Handbook

---
Data output Formats
- Analog Formats:
  - Current (e.g. 4-20mA)
  - Voltage
  - Frequency
  - Phase
- Digital Formats:
  - UART
  - I2C
  - Custom

---
SAR ADC

---
MSP430 ADC implementation
Ref: MSP430 User Manual

---
Industrial Process Control Loop
Ref: Sensor Technology Handbook

---
Sensor Installation
- EMI/EMC issues
- Cabling
- Shielding
- Enclosures

---
EMI Noise Path Model1
Noise Source
Coupling Path
Victim
How to identify noise sources?
Nodes with high dV/dt
Loops with high di/dt
HF wide band signals
Incidental transmitters like electromechanical devices
Long PCB traces/cables carrying HF signals, large loop areas
External noise sources in intended EM environment
How to identify victim circuits?
Long PCB traces/cables, large loop areas
Critical signal traces
Low power circuits where signals may hide below the noise floor
1Henry Ott, Design for Electromagnetic Compatibility
[Speaker Notes: Question 4 Intra inter Every EMI problem involves a ”source” of interference, a noise ”coupling path” and a victim [1]. EMI problem can be intrasystem with source and victim as part of same circuit (e.g. coupling between feedback control and switching circuits in an SMPS) or intersystem with distinct source circuits and victim circuits (e.g. coupling between systems sharing same power bus) [2]. Energy is radiated and/or conducted from source to victim in an EM environment A device that generates radio frequency energy during the course of its operation although the device is not intentionally designed to generate or emit radio frequency energy. Examples of incidental radiators are dc motors, mechanical light switches, etc.]

---
Noise Coupling Mechanisms
Which are the possible coupling mechanisms?
Noise may be conducted and/or radiated from source to victim
E,H Coupling
(Far Field)
Common Impedance Coupling
Capacitive, Inductive Coupling (Near Field)
Source: Deepak S, Applied Electromagnetics and Electromagnetic Compatibility
[Speaker Notes: Question 5 E ﬁeld coupling or H ﬁeld coupling when the victim is in the near ﬁeld. These modes may be represented by equivalent lumped circuit components if the circuits are electrically short (circuit dimensions are small compared to signal wavelength).]

---
Applicable Regulatory Standards for Unlicensed RF Devices
FCC Part 15
(Unlicensed RF Devices)
Subpart B
(Unintentional Radiators)
Subpart C
(Intentional Radiators)
CISPR 22
Class A Device
(Commercial, Industrial)
Class B Device
(Residential)
Class B Limits are more stringent than Class A1
1CISPR 22 Standard Documentation
[Speaker Notes: Question 2 A lot of products that historically were not wireless in nature are going to be re-engineered to become “smart.” “How do we successfully get our wireless product to market? Unlicensed radio frequency transmissions, both intentional (like a Bluetooth Smart data transmission) and unintentional (like the EM noise that a motor emits). Unintentional radiator. A device that intentionally generates radio frequency energy for use within the device, or that sends radio frequency signals by conduction to associated equipment via connecting wiring, but which is not intended to emit RF energy by radiation or induction. Incidental radiator. A device that generates radio frequency energy during the course of its operation although the device is not intentionally designed to generate or emit radio frequency energy. Examples of incidental radiators are dc motors, mechanical light switches, etc. Any product that is utilizing a wireless technology such as Wi-Fi, Bluetooth, or Zigbee will need Product Certification under FCC part 15. FCC testing for Product Certification can be broken into two parts: General Emissions testing and Intentional Radiation testing. A product that utilizes a certified RF module, such as the Bluetooth Smart module from LSR, as opposed to a discrete circuit design can leverage the certification of the shelf module and avoid the Intentional Radiation testing portion of the FCC certification process Let’s suppose your product application utilizes Bluetooth or Bluetooth Smart technologies. In addition to the regulatory requirements of the FCC to allow the sale of your product in the US, there is another regulatory body that also must be addressed: the Bluetooth Special Interest Group Class B limits are more stringent compared to Class A]

---
Typical Embedded System
Power Supply
Driver Circuits
Regulator/Power Converter
Clock
Power Source
Clock
Sensors
Analog
Front End
ADC
Digital
Circuits
RF/
Driver Circuits
Actuators
Micro
controller
Digi-tal
ADC
Analog
Front End
Sensors
[Speaker Notes: Question 6,7 Which of these blocks are most susceptible to EMI? Sensors typically remotely placed sensors/ high impedance sensors. AFE comprising of signal conditioning blocks, amplifiers Data digitization block Can you identify the possible sources of EMI in this system? Clock circuitry is usually the biggest generator of wide-band noise These are the intra system EMI sources. In a poorly designed system or a system with a poorly designed board layout, digital circuits too can act as a source of EMI. One should also look at inter system EMI sources when the product is placed in its intended EM environment. Power line cables, ambient noise sources like lightning strikes, RF broadcasts, power components such as power converters, electromechanical relays, motor drives…]

---
Demos
ADC interfacing Examples